## Slide 1: SC 19 – Machine Vision
Cameras and Interfaces
Julien VILLEMEJANE
IDS Sensor
Basler Sensor / Mouser

## Slide 2: SC19 – Cameras and Interfaces
AOP
At the end of this training, the learners will be able to:
Characterize a camera
Resolution, bit depth
Exposure Time, Black level
Digital Image, data transfer
https://iogs-lense-training.github.io/image-processing/

## Slide 3: SC19 – Cameras and Interfaces
Camera in a machine vision chain
AOP
Dong, Jing-Tao & lu, rs & Shi, Yan-Qiong & Xia, Rui-Xue & Li, Qi & Xu, Yan. (2011). Optical design of color light-emitting diode ring light for machine vision inspection. Optical Engineering - OPT ENG. 50. 10.1117/1.3567053.
Device that transforms a light flux into a measurable electrical signal
Camera
Camera
Light flux
Electrical signal

## Slide 4: SC19 – Cameras and Interfaces
Anatomy of an IDS sensor
e2v sensor EV76C560ACT
IDS UI-1240SE-C-HQ
Resolution
Sensibility
Noise Performance
Size / Form factor
Lens compatibility
Shutter Type
Interface

## Slide 5: SC19 – Cameras and Interfaces
Main charateristics of the sensor
e2v sensor EV76C560ACT

## Slide 6: SC19 – Cameras and Interfaces
Camera / Array of small sensors
Device that transforms a light flux into a measurable electrical signal
Camera
Camera
Light flux
Electrical signal
https://imaging.teledyne-e2v.com/products/2d-cmos-image-sensors/onyxmax/
1
2
3
4
1
2
3
Columns
Rows
4
5
6

## Slide 7: SC19 – Cameras and Interfaces
Camera / Bayer filter for color sensors
AOP
1
2
3
4
1
2
3
Columns
Rows
4
5
6
e2v sensor EV76C560ACT

## Slide 8: SC19 – Cameras and Interfaces
Camera / Bayer filter for color sensors
AOP
1
2
3
4
1
2
3
Columns
Rows
4
5
6
e2v sensor EV76C560ACT

## Slide 9: SC19 – Cameras and Interfaces
Camera / Inside a pixel
Device that transforms a light flux into a measurable electrical signal
Camera
Camera
Light flux
Electrical signal
Columns
Rows
Sensor
Photodiode
Light flux
Current
Amplifier
Voltage

## Slide 10: SC19 – Cameras and Interfaces
Camera / From analog to digital signal
Device that transforms an array of light flux sensors into digital data called pixels
Digital Camera
Camera
Light flux
Digital Data
Sensor
Photodiode
Light flux
Current
Amplifier
Voltage
Columns
Rows
Voltage
ADC
Digital Value

## Slide 11: SC19 – Cameras and Interfaces
How an Analog to Digital Converter works ?
Voltage
ADC
Digital Value
Analog input
voltage
Vmin
Vmax
Digital Value
ADC
Analog Input
Digital Outputs
b0
b1
b2
bn
n bits
The number of different values that can be represented by n bits is 2n.
Each bit can have one of two values: 0 or 1.
Example for n = 3 bits
quantum
0 0 0
0 0 1
1 0 1
0 1 1
1 0 0
0 1 0
1 1 0
1 1 1
Full Scale
b2 b1 b0
decimal
7
0
1
2
3
4
5
6
Quantization

## Slide 12: SC19 – Cameras and Interfaces
Sampling and quantization of an image
Voltage
ADC
Digital Value
ADC
Analog Input
Digital Outputs
b0
b1
b2
bn
n bits
The number of different values that can be represented by n bits is 2n.
Each bit can have one of two values: 0 or 1.
Quantization

## Slide 13: SC19 – Cameras and Interfaces
Sampling and quantization of an image
Voltage
ADC
Digital Value
Sampling
Area of sampling
Barcode to decode
Bad sampling rate
Not so bad sampling rate
Sampling theorem
Nyquist–Shannon sampling theorem
The sampling frequency must be equal to or greater than twice the frequency associated with the finest detail in the image (edges).
With a grid spacing of d , a periodic component with a period higher than 2.d can be reconstructed.
https://barcode-coder.com/fr/specification-ean-13-102.html

## Slide 14: SC19 – Cameras and Interfaces
Sampling and quantization of an image
Voltage
ADC
Digital Value
Sampling

## Slide 15: SC19 – Cameras and Interfaces
Camera / From analog to digital signal
Device that transforms an array of light flux sensors into digital data called pixels
Digital Camera
Camera
Light flux
Digital Data
Columns
Rows
Sensor
Photodiode
Light flux
Charges
Capacitor
Voltage
ADC
Digital Value
Sensor
Photodiode
Light flux
Current
Amplifier
Voltage

## Slide 16: SC19 – Cameras and Interfaces
Inside a real sensor
Columns
Rows
e2v sensor EV76C560ACT

## Slide 17: SC19 – Cameras and Interfaces
Quantity of data per image
Columns
Rows
Each pixel is converted into n bits.
h
v
Nb of pixels = h x v
n bits
Each image has a total amount of binary data :
Nb of data (bits) = Nb of pixels x n
Nb of pixels = 1280 x 1024
Nb of data (bits) = 1280 x 1024 x 10
= 13 107 200 bits

## Slide 18: SC19 – Cameras and Interfaces
Frame Rate
Frame rate
Each image has a total amount of binary data :
Nb of data (bits) = Nb of pixels x n
The amount of data per second :
Nb of data per s (bits/s) = Nb of data (bits) x FPS
Nb of data per s (bits/s) = 99 532 800 x 30 = 2,9 billions of bits / s = 2,78 Gbit/s
Example for a 4k camera in 12 bits @ 30 fps :
Nb of data (bits) = 3840 x 2160 x 12 = 99 532 800 bits
Number of individual frames captured per second by a device
Expressed in frames per second (fps)
Higher framerates result in smoother motion in video footage
In 2024, the transfer rate of a home router (optical fiber) is theoretically 8 Gbit/s (Free telecom - France)

## Slide 19: SC19 – Cameras and Interfaces
Interface for data transfer
AOP
The data from a camera is transferred via an interface.
There are several types of standard interfaces.
 | USB 3.0 | 10 GigE | CameraLink | Coaxpress
Bandwith | 5 to 20 Gbit/s | 1.2 Gbits/s | Base : 2 Gbits/s Full : 5.4 Gbits/s (2 cables) | 12.5 Gbits/s per cable
Cable length | 3 m | 100 m | 7 to 15 m | 20 to 40 m
Power | 4.5 to 25 W | 30 W * | Optional | 13 W / cable
Frame Grabber | Not Required | Not Required | Required | Required
GeniCam | Required | Required | Optional | Required

## Slide 20: SC19 – Cameras and Interfaces
Dark Current
Sensor
Photodiode
Light flux
Current
Amplifier
Voltage
Columns
Rows
Dark Current
Response of the sensor to complete darkness

## Slide 21: SC19 – Cameras and Interfaces
Black level : an offset to compensate electronic defaults
Sensor
Photodiode
Light flux
Current
Amplifier
Voltage
Columns
Rows
Black Level
Change the overall brightness of an image.
Adjusting the camera's black level will result in an offset to the pixel's gray values output by the camera.
Dark Current
Response of the sensor to complete darkness
+ noise
+ manufacturing process, operating temperature,…
Due to various physical and electronic factors, the sensor's output is never zero, even in the complete absence of light
Black Level
+
+

## Slide 22: SC19 – Cameras and Interfaces
Exposure Time
Exposure Time
Duration for which the camera’s sensor is exposed to light, when capturing an image.
This parameter determines the amount of light collected.
Sensor
Photodiode
Light flux
Charges
Capacitor
Voltage
Columns
Rows
ADC
Digital Value
i.e. the amount of collected charges coming from the sensor stored in a capacitor
integration
read
reset
Light flux
Charges
time
time

## Slide 23: SC19 – Cameras and Interfaces
Exposure Time
Exposure Time
Duration for which the camera’s sensor is exposed to light, when capturing an image.
This parameter determines the amount of light collected.
Sensor
Photodiode
Light flux
Charges
Capacitor
Voltage
Columns
Rows
ADC
Digital Value
i.e. the amount of collected charges coming from the sensor stored in a capacitor
integration
read
reset
Light flux
Charges
time
time

## Slide 24: SC19 – Cameras and Interfaces
Exposure Time
Exposure Time
Duration for which the camera’s sensor is exposed to light, when capturing an image.
This parameter determines the amount of light collected.
Sensor
Photodiode
Light flux
Charges
Capacitor
Voltage
Columns
Rows
ADC
Digital Value
i.e. the amount of collected charges coming from the sensor stored in a capacitor
integration
read
reset
Light flux
Charges
time
time

## Slide 25: SC19 – Cameras and Interfaces
Spatial Resolution
Spatial resolution / P
Distance observed by a single pixel in a given direction
Small object to detect
d
Security factor S
This security factor is due to the Nyquist-Shanon theorem.
And S >= 2
To verify is the spatial resolution is good enough, calibration target can be used. (Foucault)

## Slide 26: SC19 – Cameras and Interfaces
Resolution of the sensor
Spatial resolution / P
Distance observed by a single pixel in a given direction
Sensor
Inspection
Area
S
mm
pixels
Sensor resolution (pixels)
H (mm)  R (px)
d (mm)  S (px)
P (mm)  1 (px)

## Slide 27: SC19 – Cameras and Interfaces
Motion, sharp image and maximum exposure time
V : motion speed (mm/s)
V
time
position
Spatial resolution / P
Distance observed by a single pixel in a given direction
(mm)  (s)
Displacement
Time
Motion blur perception threshold
to obtain a sharp image
is between
1/2 and 1/5 of a pixel