## Slide 1: Cameras for Machine Vision
Institut d’Optique – Engineers Training
Semester 6 – Digital Interface
Julien VILLEMEJANE

## Slide 2
Cameras for Machine Vision
At the end of this training, the learners will be able to:
Describe
Resolution, bit depth
Exposure Time, Black level
Digital Image, data transfer
https://iogs-lense-training.github.io/image-processing/

## Slide 3
Cameras and Interfaces
AOP
Camera in a machine vision system
Dong, Jing-Tao & lu, rs & Shi, Yan-Qiong & Xia, Rui-Xue & Li, Qi & Xu, Yan. (2011). Optical design of color light-emitting diode ring light for machine vision inspection. Optical Engineering - OPT ENG. 50. 10.1117/1.3567053.
Device that transforms a light flux into a measurable electrical signal
Camera
Camera
Light flux
Electrical signal

## Slide 4
Cameras and Interfaces
Camera : anatomy of a sensor
e2v sensor EV76C560ACT
IDS UI-1240SE-C-HQ
Resolution
Sensibility
Noise Performance
Size / Form factor
Lens compatibility
Shutter Type
Interface

## Slide 5
Cameras and Interfaces
Main characteristics of the sensor
e2v sensor EV76C560ACT

## Slide 6
Cameras and Interfaces
Camera : array of small sensors
Device that transforms a light flux into a measurable electrical signal
Camera
Camera
Light flux
Electrical signal
https://imaging.teledyne-e2v.com/products/2d-cmos-image-sensors/onyxmax/
1
2
3
4
1
2
3
Columns
Rows
4
5
6

## Slide 7
Cameras and Interfaces
Camera : array of small sensors
1
2
3
4
1
2
3
Columns
Rows
4
5
6
e2v sensor EV76C560ACT
Resolution
Size / Form factor
Pixel size
Horizontal number of pixels (h)
Vertical number of pixels (v)

## Slide 8
Cameras and Interfaces
AOP
Camera : Bayer filter for color sensor
1
2
3
4
1
2
3
Columns
Rows
4
5
6
e2v sensor EV76C560ACT

## Slide 9
Cameras and Interfaces
Inside a pixel
Device that transforms a light flux into a measurable electrical signal
Camera
Camera
Light flux
Electrical signal
Columns
Rows
Sensor
Photodiode
Light flux
Current
Amplifier
Voltage

## Slide 10
Cameras and Interfaces
From analog signal to digital data
Device that transforms an array of light flux sensors into digital data called pixels
Digital Camera
Camera
Light flux
Digital Data
Sensor
Photodiode
Light flux
Current
Amplifier
Voltage
Columns
Rows
Voltage
ADC
Digital Value

## Slide 11
Cameras and Interfaces
How an Analog to Digital Converter works ?
Voltage
ADC
Digital Value
Analog input
voltage
Vmin
Vmax
Digital Value
ADC
Analog Input
Digital Outputs
b0
b1
b2
bn
n bits
The number of different values that can be represented by n bits is 2n.
Each bit can have one of two values: 0 or 1.
Example for n = 3 bits
quantum
0 0 0
0 0 1
1 0 1
0 1 1
1 0 0
0 1 0
1 1 0
1 1 1
Full Scale
b2 b1 b0
decimal
7
0
1
2
3
4
5
6
Quantification

## Slide 12
Cameras and Interfaces
How an Analog to Digital Converter works ?
Voltage
ADC
Digital Value
ADC
Analog Input
Digital Outputs
b0
b1
b2
bn
n bits
The number of different values that can be represented by n bits is 2n.
Each bit can have one of two values: 0 or 1.
Quantification

## Slide 13
Cameras and Interfaces
Sampling and quantification of an image
Voltage
ADC
Digital Value
Sampling
Area of sampling
Barcode to decode
Bad sampling rate
Not so bad sampling rate
Sampling theorem
Nyquist–Shannon sampling theorem
The sampling frequency must be equal to or greater than twice the frequency associated with the finest detail in the image (edges).
With a grid spacing of d , a periodic component with a period higher than 2.d can be reconstructed.
https://barcode-coder.com/fr/specification-ean-13-102.html

## Slide 14
Cameras and Interfaces
Sampling and quantification of an image
Voltage
ADC
Digital Value
Sampling

## Slide 15
Cameras and Interfaces
Camera : array of small sensors
The number of different values that can be represented by 10 bits is 210 = 1024
In a Grayscale mode :
a black pixel is represented by 0
a white pixel is represented by 1023
Full scale of the ADC is 12 ke-

## Slide 16
Cameras and Interfaces
Inside a real camera
Columns
Rows
e2v sensor EV76C560ACT

## Slide 17
Cameras and Interfaces
Amount of data per image
Columns
Rows
Each pixel is converted into n bits.
h
v
Nb of pixels = h x v
n bits
Each image has a total amount of binary data :
Nb of data (bits) = Nb of pixels x n

## Slide 18
Cameras and Interfaces
Amount of data per image
Columns
Rows
Each pixel is converted into n bits.
h
v
Nb of pixels = h x v
n bits
Each image has a total amount of binary data :
Nb of data (bits) = Nb of pixels x n
Nb of pixels = 1280 x 1024
Nb of data (bits) = 1280 x 1024 x 10
= 13 107 200 bits

## Slide 19
Cameras and Interfaces
Frame rate
Frame rate
Each image has a total amount of binary data :
Nb of data (bits) = Nb of pixels x n
The amount of data per second :
Nb of data per s (bits/s) = Nb of data (bits) x FPS
Nb of data per s (bits/s) = 99 532 800 x 30 = 2,9 billions of bits / s = 2,78 Gbit/s
Example for a 4k camera in 12 bits @ 30 fps :
Nb of data (bits) = 3840 x 2160 x 12 = 99 532 800 bits
Number of individual frames captured per second by a device
Expressed in frames per second (fps)
Higher framerates result in smoother motion in video footage
In 2024, the transfer rate of a home router (optical fiber) is theoretically 8 Gbit/s (Free telecom - France)

## Slide 20
Cameras and Interfaces
AOP
Interface for data transfer
The data from a camera is transferred via an interface.
There are several types of standard interfaces.
 | USB 3.0 | 10 GigE | CameraLink | Coaxpress
Bandwith | 5 to 20 Gbit/s | 1.2 Gbits/s | Base : 2 Gbits/s Full : 5.4 Gbits/s (2 cables) | 12.5 Gbits/s per cable
Cable length | 3 m | 100 m | 7 to 15 m | 20 to 40 m
Power | 4.5 to 25 W | 30 W * | Optional | 13 W / cable
Frame Grabber | Not Required | Not Required | Required | Required
GeniCam | Required | Required | Optional | Required

## Slide 21
Cameras and Interfaces
Dark current
Sensor
Photodiode
Light flux
Current
Amplifier
Voltage
Columns
Rows
Dark Current
Response of the sensor to complete darkness

## Slide 22
Cameras and Interfaces
Black level : an offset to compensate electronic defaults
Sensor
Photodiode
Light flux
Current
Amplifier
Voltage
Columns
Rows
Black Level
Change the overall brightness of an image.
Adjusting the camera's black level will result in an offset to the pixel's gray values output by the camera.
Dark Current
Response of the sensor to complete darkness
+ noise
+ manufacturing process, operating temperature,…
Due to various physical and electronic factors, the sensor's output is never zero, even in the complete absence of light
Black Level
+
+

## Slide 23
Cameras and Interfaces
Exposure time and linearity
Exposure Time
Duration for which the camera’s sensor is exposed to light, when capturing an image.
This parameter determines the amount of light collected.
Sensor
Photodiode
Light flux
Current
Amplifier
Voltage
Columns
Rows

## Slide 24
Cameras and Interfaces
Spatial resolution
Spatial resolution / P
Distance observed by a single pixel in a given direction
Small object to detect
d
Security factor S
This security factor is due to the Nyquist-Shanon theorem.
And S >= 2
To verify is the spatial resolution is good enough, calibration target can be used. (Foucault)

## Slide 25
Cameras and Interfaces
Resolution of the sensor
Spatial resolution / P
Distance observed by a single pixel in a given direction
Sensor
Inspection
Area
S
mm
pixels
Sensor resolution (pixels)
H (mm)  R (px)
d (mm)  S (px)
P (mm)  1 (px)

## Slide 26
Cameras and Interfaces
Motion, sharp image and maximum exposure time
V : motion speed (mm/s)
V
time
position
Spatial resolution / P
Distance observed by a single pixel in a given direction
(mm)  (s)
Displacement
Time
Motion blur perception threshold
to obtain a sharp image
is between
1/2 and 1/5 of a pixel

## Slide 27
Cameras and Interfaces
AOP
Bayer filter and image reconstruction
1
2
3
4
1
2
3
Columns
Rows
4
5
6
e2v sensor EV76C560ACT
Interpolation