## Slide 1: SC19 Image processing with OpenCV
Institut d’Optique
Formation Continue
Julien VILLEMEJANE

## Slide 2
SC19 – Image processing / OpenCV
At the end of this training, the learners will be able to:
Use basic building blocks of OpenCV
Open an image
Create the histogram of an image
Apply basic transforms on images
- blur, filters
- erosion, dilation, opening, closing
Display the contour of objects
https://iogs-lense-training.github.io/image-processing/

## Slide 3
SC19 – Image processing
What is image processing for ?
Why is image processing required in a machine vision chain ?
For industrial inspection applications ?
What are the main processes ?
What is the goal of each of them ?
What is the ideal workflow ?
https://www.youtube.com/@firstprinciplesofcomputerv3258

## Slide 4
SC19 – Image processing
Goal of processing an image
Image from the camera
Noise
Bad contrast
Inhomogeneous Lighting
…
Desired image with objects with well-defined contours
Homogeneous zones
Transition zones
Notes: In a machine vision inspection application, the image processing pipeline involves a series of steps that transform raw image data into meaningful decisions about product quality or other criteria. Here’s an overview of the main steps from capturing the image to making a decision:
### 1. **Image Acquisition**
- **Camera Setup**: A camera captures images of the product or material. This could involve multiple cameras or 3D sensors, depending on the application.
- **Lighting Control**: Appropriate lighting ensures consistent and accurate image capture, helping highlight defects or features.
- **Triggering**: The image is typically captured when the product reaches a specific point on a conveyor belt (triggered by sensors).
### 2. **Preprocessing**
- **Noise Reduction**: Filters are applied to reduce noise in the image (e.g., smoothing, Gaussian filters), ensuring clarity and reducing unwanted information.
- **Contrast Enhancement**: Adjusting the image contrast or brightness to make features of interest stand out.
- **Normalization**: Standardizing the image scale or intensity to create consistency across multiple images for easier analysis.
### 3. **Segmentation**
- **Thresholding**: Convert the image to a binary or multi-level image to isolate objects or regions of interest (e.g., separate a product from the background).
- **Edge Detection**: Detect the edges of objects or features in the image, which is useful for identifying boundaries and contours.
- **Region of Interest (ROI) Selection**: Select specific areas of the image for further processing, focusing only on relevant portions of the image.
### 4. **Feature Extraction**
- **Geometric Features**: Extract measurements like size, shape, position, orientation, and symmetry from the segmented objects.
- **Texture Analysis**: Analyze the texture patterns for roughness, uniformity, etc., to assess the surface quality.
- **Color Analysis**: Extract color information for color-based inspection, ensuring the correct color is used or verifying its consistency.
- **Pattern Recognition**: Recognize patterns, symbols, or specific features to classify parts or detect defects.
### 5. **Object Detection and Classification**
- **Object Detection**: Identify and label objects within the image to confirm their presence or detect defects.
- **Template Matching**: Match the object or part in the image against a predefined template to check for correct shape, size, and orientation.
- **Classification**: Based on the extracted features, classify the objects as good, bad, or categorize them into specific groups (e.g., defective or non-defective).
### 6. **Decision Making**
- **Comparison Against Tolerances**: The extracted measurements, shapes, and features are compared against predefined tolerances or quality standards.
- **Pass/Fail Decision**: Based on the comparison, a decision is made whether the product meets the required quality standards. If it fails, the system can trigger corrective actions (e.g., rejecting the item or sending it for rework).
- **Real-time Feedback**: Provide real-time feedback to the production system to either pass or reject the part or trigger alarms if defects are detected.
### 7. **Post-processing and Output**
- **Data Logging**: Record the inspection data and images for further analysis or auditing purposes.
- **Output to Control Systems**: The decision is communicated to automated systems such as conveyor belts, robotic arms, or quality control stations to handle the product accordingly.
- **Operator Interface**: The results and images are often displayed on a graphical interface for human operators to monitor the process.
### 8. **Feedback and Learning (Optional)**
- In some advanced systems, **machine learning** or **AI algorithms** are used to adapt and improve decision-making over time by learning from previous images and inspection outcomes.
This image processing pipeline ensures fast, accurate, and repeatable inspection in manufacturing environments, reducing human error and improving overall product quality.

## Slide 5
SC19 – Image processing
Steps for processing an image
Acquisition
Pre Processing
Segmentation
Feature Extraction
Classification
Decision
Noise Reduction / Filtering
Contrast Enhancement
Normalization
Ensuring clarity and reducing unwanted information
Making features of interest stand out
Standardizing the image scale or intensity
Thresholding
Edge Detection
Region of Interest Selection
Geometric Features
Texture Analysis
Color Analysis
Isolating objects of ROI / Separating product from background
Identifying boundaries and contours
Focusing only on relevant portions of the image
Extracting measurements (size, shape, position…)
Recognizing patterns, symbols, points of interest
Object detection
Template Matching
Classification
Identifying and labelling objects
Checking correct shape, size or orientation
Categorizing objects to specific groups (defective or non-def.)
Tolerances, pass/fail, real-time feedback…
Light, Camera…
Notes: In a machine vision inspection application, the image processing pipeline involves a series of steps that transform raw image data into meaningful decisions about product quality or other criteria. Here’s an overview of the main steps from capturing the image to making a decision:
### 1. **Image Acquisition**
- **Camera Setup**: A camera captures images of the product or material. This could involve multiple cameras or 3D sensors, depending on the application.
- **Lighting Control**: Appropriate lighting ensures consistent and accurate image capture, helping highlight defects or features.
- **Triggering**: The image is typically captured when the product reaches a specific point on a conveyor belt (triggered by sensors).
### 2. **Preprocessing**
- **Noise Reduction**: Filters are applied to reduce noise in the image (e.g., smoothing, Gaussian filters), ensuring clarity and reducing unwanted information.
- **Contrast Enhancement**: Adjusting the image contrast or brightness to make features of interest stand out.
- **Normalization**: Standardizing the image scale or intensity to create consistency across multiple images for easier analysis.
### 3. **Segmentation**
- **Thresholding**: Convert the image to a binary or multi-level image to isolate objects or regions of interest (e.g., separate a product from the background).
- **Edge Detection**: Detect the edges of objects or features in the image, which is useful for identifying boundaries and contours.
- **Region of Interest (ROI) Selection**: Select specific areas of the image for further processing, focusing only on relevant portions of the image.
### 4. **Feature Extraction**
- **Geometric Features**: Extract measurements like size, shape, position, orientation, and symmetry from the segmented objects.
- **Texture Analysis**: Analyze the texture patterns for roughness, uniformity, etc., to assess the surface quality.
- **Color Analysis**: Extract color information for color-based inspection, ensuring the correct color is used or verifying its consistency.
- **Pattern Recognition**: Recognize patterns, symbols, or specific features to classify parts or detect defects.
### 5. **Object Detection and Classification**
- **Object Detection**: Identify and label objects within the image to confirm their presence or detect defects.
- **Template Matching**: Match the object or part in the image against a predefined template to check for correct shape, size, and orientation.
- **Classification**: Based on the extracted features, classify the objects as good, bad, or categorize them into specific groups (e.g., defective or non-defective).
### 6. **Decision Making**
- **Comparison Against Tolerances**: The extracted measurements, shapes, and features are compared against predefined tolerances or quality standards.
- **Pass/Fail Decision**: Based on the comparison, a decision is made whether the product meets the required quality standards. If it fails, the system can trigger corrective actions (e.g., rejecting the item or sending it for rework).
- **Real-time Feedback**: Provide real-time feedback to the production system to either pass or reject the part or trigger alarms if defects are detected.
### 7. **Post-processing and Output**
- **Data Logging**: Record the inspection data and images for further analysis or auditing purposes.
- **Output to Control Systems**: The decision is communicated to automated systems such as conveyor belts, robotic arms, or quality control stations to handle the product accordingly.
- **Operator Interface**: The results and images are often displayed on a graphical interface for human operators to monitor the process.
### 8. **Feedback and Learning (Optional)**
- In some advanced systems, **machine learning** or **AI algorithms** are used to adapt and improve decision-making over time by learning from previous images and inspection outcomes.
This image processing pipeline ensures fast, accurate, and repeatable inspection in manufacturing environments, reducing human error and improving overall product quality.

## Slide 6: SC19 OpenCV
Institut d’Optique
Formation Continue

## Slide 7
SC19 – Image processing with OpenCV
AOP
What is OpenCV ?
http://opencv.org
Open Source Computer Vision Library
An open source computer vision and machine learning software library
supporting multiple programming languages such as Python, C++, Java, and MATLAB
Image Processing
Object Recognition
CV Algorithms
Filtering, Edge detection, Image transformations…
Detecting objects in images and videos
Motion tracking, 3D reconstruction, Augmented reality
Machine Learning
Image classification, Pattern recognition, Scene Understanding
OpenCV 4.5.0 and higher versions are licensed under the Apache 2 License.
OpenCV 4.4.0 and lower versions, including OpenCV 3.x, OpenCV 2.x, and OpenCV 1.x, are licensed under the 3-clause BSD license.

## Slide 8
SC19 – Image processing with OpenCV
AOP
Python 3 and OpenCV
https://iogs-lense-training.github.io/image-processing/
http://opencv.org
pip install opencv-python
import cv2
Cv2.__version__
Installing OpenCV for Python 3
Testing OpenCV importation in a script

## Slide 9: SC19 Digital Images And processings
Institut d’Optique
Formation Continue

## Slide 10
SC19 – Image processing with OpenCV
AOP
Digital Images / Resolution
1
2
3
4
1
2
3
1
2
3
4
1
2
3
R
G
B
GrayScale
Columns
Rows
Nb of pixels = h x v

## Slide 11
SC19 – Image processing with OpenCV
AOP
Digital Images / Depth
1
2
3
4
1
2
3
GrayScale
Columns
Rows
Each pixel is converted into n bits.
Nb of pixels = h x v
RGB : 3 channels of 8 bits
1
2
3
4
1
2
3
R=200, G=100, G=50
R
G
B

## Slide 12
SC19 – Image processing with OpenCV
Digital Images / Color Spaces
Color Space
Model for representing colors in a consistent and reproducible way
Each color space uses a different method for organizing and describing color, depending on the purpose or application
RGB
Used primarily in electronic displays like computer screens, cameras, and scanners. The combination of these three primary colors at various intensities can produce any color.
Images Source : Wikipedia
HSV
Used in image editing. It separates image’s color from its brightness.
Hue : type of color
Saturation : intensity of the color
Value : Brightness of the color
CMYK
LAB
YUV

## Slide 13
SC19 – Image processing with OpenCV
Digital Images / Color Spaces
Table 9 from
Segmentation of Images by Color Features: A Survey - Scientific Figure on ResearchGate. Available from: https://www.researchgate.net/figure/Advantages-and-disadvantages-of-color-spaces_tbl7_323632019 [accessed 10 Oct 2024]
Color Space
Model for representing colors in a consistent and reproducible way

## Slide 14
cv2.imshow('Image ', image_rgb)
cv2.waitKey(0)
SC19 – Image processing with OpenCV
OpenCV / Open and display an Image
import cv2
image_rgb = cv2.imread(‘path/to/image.png’)
image_gray = cv2.imread(‘path/to/image.png’, cv2.IMREAD_GRAYSCALE)
Acquisition

## Slide 15
SC19 – Image processing with OpenCV
Pre-Processing
Pre Processing
Acquisition
Noise Reduction / Filtering
Contrast Enhancement
Normalization
Ensuring clarity and reducing unwanted information
Making features of interest stand out
Standardizing the image scale or intensity

## Slide 16
SC19 – Image processing with OpenCV
OpenCV / Histogram of an image
Pre Processing
Acquisition
Histogram
Graphical representation that shows the distribution of pixel intensity values in an image
cv2.calcHist([image], [chan], Mask, [bins_nb], [min, max])

## Slide 17
SC19 – Image processing with OpenCV
OpenCV / Contrast and Brightness
Pre Processing
Acquisition
new_img = cv2.convertScaleAbs(image, beta=100)
+ 100
+ 100
+ 100
+ 100

## Slide 18
SC19 – Image processing with OpenCV
OpenCV / Contrast and Brightness
Pre Processing
Acquisition
new_img = cv2.convertScaleAbs(image, alpha=1.5)
x 1.5
x 1.5
x 1.5
x 1.5

## Slide 19
SC19 – Image processing with OpenCV
OpenCV / Convolution
Pre Processing
Acquisition
Convolution (filter)
5
8
9
5
4
2
1
8
3
1
7
6
5
7
5
8
1
5
2
8
6
8
4
3
5
6
6
7
2
5
5
2
7
3
1
-1
0
1
-2
1
-2
0
-1
kernel
original image
filtered image
4
5
8
9
5
4
2
1
3
1
5
7
5
8
1
2
5
6
6
7
2
5
5
2
7
3
1
8
-1
x
5
7
0
x
6
-2
x
5
1
x
6
5
x
8
1
x
8
-2
x
4
0
x
3
-1
x
R = -8 + 0 – 12 + 5 + 30 + 8 – 16 + 0 – 3
R = 4

## Slide 20
SC19 – Image processing with OpenCV
OpenCV / Convolution Kernel (or Structuring Element)
Pre Processing
Acquisition
0
1
1
0
1
0
1
0
Cross Kernel
1
0
1
0
0
1
0
0
1
0
0
0
0
1
0
0
0
1
1
1
1
1
1
1
1
Rect Kernel
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
cv2.MORPH_RECT
cv2.MORPH_CROSS
kernel = cv2.getStructuringElement(cv2.MORPH_xx, (M,N))

## Slide 21
SC19 – Image processing with OpenCV
OpenCV / Erosion and Dilation
Pre Processing
Acquisition
0
1
1
0
1
0
1
0
kernel
1
https://www.youtube.com/watch?v=fmyE7DiaIYQ
https://www.youtube.com/watch?v=xO3ED27rMHs
Original pixels
Removed pixels
Added pixels
Dilation
Enlarging the foreground by adding pixels to the boundaries of objects
Erosion
Shrinking the foreground by removing pixels to the boundaries of objects

## Slide 22
SC19 – Image processing with OpenCV
OpenCV / Erosion and Dilation
Pre Processing
Acquisition
0
1
1
0
1
0
1
0
kernel
1
Dilation
Enlarging the foreground by adding pixels to the boundaries of objects
Erosion
Shrinking the foreground by removing pixels to the boundaries of objects
eroded_image = cv2.erode(image, kernel, iterations=1)
dilated_image = cv2.dilate(image, kernel, iterations=1)

## Slide 23
SC19 – Image processing with OpenCV
OpenCV / Opening and Closing morphological transforms
Pre Processing
Acquisition
0
1
1
0
1
0
1
0
kernel
1
Closing
Dilation then Erosion
Filling in small holes
Opening
Erosion then Dilation
Removing small objects
Original pixels
Removed pixels
Added pixels

## Slide 24
SC19 – Image processing with OpenCV
OpenCV / Opening and Closing morphological transforms
Pre Processing
Acquisition
0
1
1
0
1
0
1
0
kernel
1
Closing
Dilation then Erosion
Filling in small holes
Opening
Erosion then Dilation
Removing small objects
opening_image = cv2.morphologyEx(image, cv2.MORPH_OPEN, kernel)
closing_image = cv2.morphologyEx(image, cv2.MORPH_CLOSE, kernel)

## Slide 25
SC19 – Image processing with OpenCV
OpenCV / Opening and Closing morphological transforms
Pre Processing
Acquisition
0
1
1
0
1
0
1
0
kernel
1
Dilation then Erosion
Filling in small holes in the foreground
Erosion then Dilation
Removing small objects, in the background
Closing
Opening
opening_image = cv2.morphologyEx(image, cv2.MORPH_OPEN, kernel)
closing_image = cv2.morphologyEx(image, cv2.MORPH_CLOSE, kernel)

## Slide 26
SC19 – Image processing with OpenCV
OpenCV / Gradient morphological transforms
Pre Processing
Acquisition
0
1
1
0
1
0
1
0
kernel
1
gradient_image = cv2.morphologyEx(image, cv2.MORPH_GRADIENT, kernel)
Gradient
Difference between a dilation and an erosion
Unknown pixels classification : background or foreground ?

## Slide 27
1/9
1
SC19 – Image processing with OpenCV
OpenCV / Blur and mean
cv2.imshow('Image Window', image)
Pre Processing
Acquisition
16
26
26
16
26
16
26
16
41
4
7
4
4
7
4
4
7
4
1
4
7
4
1
1
Gaussian Kernel
(x 1/273)
Mean Kernel ( x 1/(N*M) )
1/9
1/9
1/9
1/9
1/9
1/9
1/9
1/9
kernel_size = (N,M)
blurred_image_gauss = cv2.GaussianBlur(image, kernel_size, 0)
blurred_image_box = cv2.blur(image, kernel_size)
Removing irrelevant details

## Slide 28
SC19 – Image processing
Goal of processing an image
Acquisition
Pre Processing
Segmentation
Thresholding
Edge Detection
Region of Interest Selection
Isolating objects of ROI / Separating product from background
Identifying boundaries and contours
Focusing only on relevant portions of the image
Feature Extraction
Geometric Features
Texture Analysis
Color Analysis
Extracting measurements (size, shape, position…)
Recognizing patterns, symbols, points of interest
https://docs.opencv.org/4.x/d3/db4/tutorial_py_watershed.html
Notes: In a machine vision inspection application, the image processing pipeline involves a series of steps that transform raw image data into meaningful decisions about product quality or other criteria. Here’s an overview of the main steps from capturing the image to making a decision:
### 1. **Image Acquisition**
- **Camera Setup**: A camera captures images of the product or material. This could involve multiple cameras or 3D sensors, depending on the application.
- **Lighting Control**: Appropriate lighting ensures consistent and accurate image capture, helping highlight defects or features.
- **Triggering**: The image is typically captured when the product reaches a specific point on a conveyor belt (triggered by sensors).
### 2. **Preprocessing**
- **Noise Reduction**: Filters are applied to reduce noise in the image (e.g., smoothing, Gaussian filters), ensuring clarity and reducing unwanted information.
- **Contrast Enhancement**: Adjusting the image contrast or brightness to make features of interest stand out.
- **Normalization**: Standardizing the image scale or intensity to create consistency across multiple images for easier analysis.
### 3. **Segmentation**
- **Thresholding**: Convert the image to a binary or multi-level image to isolate objects or regions of interest (e.g., separate a product from the background).
- **Edge Detection**: Detect the edges of objects or features in the image, which is useful for identifying boundaries and contours.
- **Region of Interest (ROI) Selection**: Select specific areas of the image for further processing, focusing only on relevant portions of the image.
### 4. **Feature Extraction**
- **Geometric Features**: Extract measurements like size, shape, position, orientation, and symmetry from the segmented objects.
- **Texture Analysis**: Analyze the texture patterns for roughness, uniformity, etc., to assess the surface quality.
- **Color Analysis**: Extract color information for color-based inspection, ensuring the correct color is used or verifying its consistency.
- **Pattern Recognition**: Recognize patterns, symbols, or specific features to classify parts or detect defects.
### 5. **Object Detection and Classification**
- **Object Detection**: Identify and label objects within the image to confirm their presence or detect defects.
- **Template Matching**: Match the object or part in the image against a predefined template to check for correct shape, size, and orientation.
- **Classification**: Based on the extracted features, classify the objects as good, bad, or categorize them into specific groups (e.g., defective or non-defective).
### 6. **Decision Making**
- **Comparison Against Tolerances**: The extracted measurements, shapes, and features are compared against predefined tolerances or quality standards.
- **Pass/Fail Decision**: Based on the comparison, a decision is made whether the product meets the required quality standards. If it fails, the system can trigger corrective actions (e.g., rejecting the item or sending it for rework).
- **Real-time Feedback**: Provide real-time feedback to the production system to either pass or reject the part or trigger alarms if defects are detected.
### 7. **Post-processing and Output**
- **Data Logging**: Record the inspection data and images for further analysis or auditing purposes.
- **Output to Control Systems**: The decision is communicated to automated systems such as conveyor belts, robotic arms, or quality control stations to handle the product accordingly.
- **Operator Interface**: The results and images are often displayed on a graphical interface for human operators to monitor the process.
### 8. **Feedback and Learning (Optional)**
- In some advanced systems, **machine learning** or **AI algorithms** are used to adapt and improve decision-making over time by learning from previous images and inspection outcomes.
This image processing pipeline ensures fast, accurate, and repeatable inspection in manufacturing environments, reducing human error and improving overall product quality.

## Slide 29
SC19 – Image processing
Segmentation and Feature Extraction
Acquisition
Pre Processing
Segmentation
Feature Extraction
Watershed method
Notes: In a machine vision inspection application, the image processing pipeline involves a series of steps that transform raw image data into meaningful decisions about product quality or other criteria. Here’s an overview of the main steps from capturing the image to making a decision:
### 1. **Image Acquisition**
- **Camera Setup**: A camera captures images of the product or material. This could involve multiple cameras or 3D sensors, depending on the application.
- **Lighting Control**: Appropriate lighting ensures consistent and accurate image capture, helping highlight defects or features.
- **Triggering**: The image is typically captured when the product reaches a specific point on a conveyor belt (triggered by sensors).
### 2. **Preprocessing**
- **Noise Reduction**: Filters are applied to reduce noise in the image (e.g., smoothing, Gaussian filters), ensuring clarity and reducing unwanted information.
- **Contrast Enhancement**: Adjusting the image contrast or brightness to make features of interest stand out.
- **Normalization**: Standardizing the image scale or intensity to create consistency across multiple images for easier analysis.
### 3. **Segmentation**
- **Thresholding**: Convert the image to a binary or multi-level image to isolate objects or regions of interest (e.g., separate a product from the background).
- **Edge Detection**: Detect the edges of objects or features in the image, which is useful for identifying boundaries and contours.
- **Region of Interest (ROI) Selection**: Select specific areas of the image for further processing, focusing only on relevant portions of the image.
### 4. **Feature Extraction**
- **Geometric Features**: Extract measurements like size, shape, position, orientation, and symmetry from the segmented objects.
- **Texture Analysis**: Analyze the texture patterns for roughness, uniformity, etc., to assess the surface quality.
- **Color Analysis**: Extract color information for color-based inspection, ensuring the correct color is used or verifying its consistency.
- **Pattern Recognition**: Recognize patterns, symbols, or specific features to classify parts or detect defects.
### 5. **Object Detection and Classification**
- **Object Detection**: Identify and label objects within the image to confirm their presence or detect defects.
- **Template Matching**: Match the object or part in the image against a predefined template to check for correct shape, size, and orientation.
- **Classification**: Based on the extracted features, classify the objects as good, bad, or categorize them into specific groups (e.g., defective or non-defective).
### 6. **Decision Making**
- **Comparison Against Tolerances**: The extracted measurements, shapes, and features are compared against predefined tolerances or quality standards.
- **Pass/Fail Decision**: Based on the comparison, a decision is made whether the product meets the required quality standards. If it fails, the system can trigger corrective actions (e.g., rejecting the item or sending it for rework).
- **Real-time Feedback**: Provide real-time feedback to the production system to either pass or reject the part or trigger alarms if defects are detected.
### 7. **Post-processing and Output**
- **Data Logging**: Record the inspection data and images for further analysis or auditing purposes.
- **Output to Control Systems**: The decision is communicated to automated systems such as conveyor belts, robotic arms, or quality control stations to handle the product accordingly.
- **Operator Interface**: The results and images are often displayed on a graphical interface for human operators to monitor the process.
### 8. **Feedback and Learning (Optional)**
- In some advanced systems, **machine learning** or **AI algorithms** are used to adapt and improve decision-making over time by learning from previous images and inspection outcomes.
This image processing pipeline ensures fast, accurate, and repeatable inspection in manufacturing environments, reducing human error and improving overall product quality.

## Slide 30
SC19 – Image processing
Segmentation and Feature Extraction
Acquisition
Pre Processing
Segmentation
Feature Extraction
Watershed method / First step - Thresholding
Notes: In a machine vision inspection application, the image processing pipeline involves a series of steps that transform raw image data into meaningful decisions about product quality or other criteria. Here’s an overview of the main steps from capturing the image to making a decision:
### 1. **Image Acquisition**
- **Camera Setup**: A camera captures images of the product or material. This could involve multiple cameras or 3D sensors, depending on the application.
- **Lighting Control**: Appropriate lighting ensures consistent and accurate image capture, helping highlight defects or features.
- **Triggering**: The image is typically captured when the product reaches a specific point on a conveyor belt (triggered by sensors).
### 2. **Preprocessing**
- **Noise Reduction**: Filters are applied to reduce noise in the image (e.g., smoothing, Gaussian filters), ensuring clarity and reducing unwanted information.
- **Contrast Enhancement**: Adjusting the image contrast or brightness to make features of interest stand out.
- **Normalization**: Standardizing the image scale or intensity to create consistency across multiple images for easier analysis.
### 3. **Segmentation**
- **Thresholding**: Convert the image to a binary or multi-level image to isolate objects or regions of interest (e.g., separate a product from the background).
- **Edge Detection**: Detect the edges of objects or features in the image, which is useful for identifying boundaries and contours.
- **Region of Interest (ROI) Selection**: Select specific areas of the image for further processing, focusing only on relevant portions of the image.
### 4. **Feature Extraction**
- **Geometric Features**: Extract measurements like size, shape, position, orientation, and symmetry from the segmented objects.
- **Texture Analysis**: Analyze the texture patterns for roughness, uniformity, etc., to assess the surface quality.
- **Color Analysis**: Extract color information for color-based inspection, ensuring the correct color is used or verifying its consistency.
- **Pattern Recognition**: Recognize patterns, symbols, or specific features to classify parts or detect defects.
### 5. **Object Detection and Classification**
- **Object Detection**: Identify and label objects within the image to confirm their presence or detect defects.
- **Template Matching**: Match the object or part in the image against a predefined template to check for correct shape, size, and orientation.
- **Classification**: Based on the extracted features, classify the objects as good, bad, or categorize them into specific groups (e.g., defective or non-defective).
### 6. **Decision Making**
- **Comparison Against Tolerances**: The extracted measurements, shapes, and features are compared against predefined tolerances or quality standards.
- **Pass/Fail Decision**: Based on the comparison, a decision is made whether the product meets the required quality standards. If it fails, the system can trigger corrective actions (e.g., rejecting the item or sending it for rework).
- **Real-time Feedback**: Provide real-time feedback to the production system to either pass or reject the part or trigger alarms if defects are detected.
### 7. **Post-processing and Output**
- **Data Logging**: Record the inspection data and images for further analysis or auditing purposes.
- **Output to Control Systems**: The decision is communicated to automated systems such as conveyor belts, robotic arms, or quality control stations to handle the product accordingly.
- **Operator Interface**: The results and images are often displayed on a graphical interface for human operators to monitor the process.
### 8. **Feedback and Learning (Optional)**
- In some advanced systems, **machine learning** or **AI algorithms** are used to adapt and improve decision-making over time by learning from previous images and inspection outcomes.
This image processing pipeline ensures fast, accurate, and repeatable inspection in manufacturing environments, reducing human error and improving overall product quality.

## Slide 31
SC19 – Image processing
Segmentation and Feature Extraction
Acquisition
Pre Processing
Segmentation
Feature Extraction
Watershed method / Third step – Labelling
Watershed method / Second step – Sure BG/FG image
Notes: In a machine vision inspection application, the image processing pipeline involves a series of steps that transform raw image data into meaningful decisions about product quality or other criteria. Here’s an overview of the main steps from capturing the image to making a decision:
### 1. **Image Acquisition**
- **Camera Setup**: A camera captures images of the product or material. This could involve multiple cameras or 3D sensors, depending on the application.
- **Lighting Control**: Appropriate lighting ensures consistent and accurate image capture, helping highlight defects or features.
- **Triggering**: The image is typically captured when the product reaches a specific point on a conveyor belt (triggered by sensors).
### 2. **Preprocessing**
- **Noise Reduction**: Filters are applied to reduce noise in the image (e.g., smoothing, Gaussian filters), ensuring clarity and reducing unwanted information.
- **Contrast Enhancement**: Adjusting the image contrast or brightness to make features of interest stand out.
- **Normalization**: Standardizing the image scale or intensity to create consistency across multiple images for easier analysis.
### 3. **Segmentation**
- **Thresholding**: Convert the image to a binary or multi-level image to isolate objects or regions of interest (e.g., separate a product from the background).
- **Edge Detection**: Detect the edges of objects or features in the image, which is useful for identifying boundaries and contours.
- **Region of Interest (ROI) Selection**: Select specific areas of the image for further processing, focusing only on relevant portions of the image.
### 4. **Feature Extraction**
- **Geometric Features**: Extract measurements like size, shape, position, orientation, and symmetry from the segmented objects.
- **Texture Analysis**: Analyze the texture patterns for roughness, uniformity, etc., to assess the surface quality.
- **Color Analysis**: Extract color information for color-based inspection, ensuring the correct color is used or verifying its consistency.
- **Pattern Recognition**: Recognize patterns, symbols, or specific features to classify parts or detect defects.
### 5. **Object Detection and Classification**
- **Object Detection**: Identify and label objects within the image to confirm their presence or detect defects.
- **Template Matching**: Match the object or part in the image against a predefined template to check for correct shape, size, and orientation.
- **Classification**: Based on the extracted features, classify the objects as good, bad, or categorize them into specific groups (e.g., defective or non-defective).
### 6. **Decision Making**
- **Comparison Against Tolerances**: The extracted measurements, shapes, and features are compared against predefined tolerances or quality standards.
- **Pass/Fail Decision**: Based on the comparison, a decision is made whether the product meets the required quality standards. If it fails, the system can trigger corrective actions (e.g., rejecting the item or sending it for rework).
- **Real-time Feedback**: Provide real-time feedback to the production system to either pass or reject the part or trigger alarms if defects are detected.
### 7. **Post-processing and Output**
- **Data Logging**: Record the inspection data and images for further analysis or auditing purposes.
- **Output to Control Systems**: The decision is communicated to automated systems such as conveyor belts, robotic arms, or quality control stations to handle the product accordingly.
- **Operator Interface**: The results and images are often displayed on a graphical interface for human operators to monitor the process.
### 8. **Feedback and Learning (Optional)**
- In some advanced systems, **machine learning** or **AI algorithms** are used to adapt and improve decision-making over time by learning from previous images and inspection outcomes.
This image processing pipeline ensures fast, accurate, and repeatable inspection in manufacturing environments, reducing human error and improving overall product quality.

## Slide 32
SC19 – Image processing
Segmentation and Feature Extraction
Acquisition
Pre Processing
Segmentation
Feature Extraction
Watershed method
Notes: In a machine vision inspection application, the image processing pipeline involves a series of steps that transform raw image data into meaningful decisions about product quality or other criteria. Here’s an overview of the main steps from capturing the image to making a decision:
### 1. **Image Acquisition**
- **Camera Setup**: A camera captures images of the product or material. This could involve multiple cameras or 3D sensors, depending on the application.
- **Lighting Control**: Appropriate lighting ensures consistent and accurate image capture, helping highlight defects or features.
- **Triggering**: The image is typically captured when the product reaches a specific point on a conveyor belt (triggered by sensors).
### 2. **Preprocessing**
- **Noise Reduction**: Filters are applied to reduce noise in the image (e.g., smoothing, Gaussian filters), ensuring clarity and reducing unwanted information.
- **Contrast Enhancement**: Adjusting the image contrast or brightness to make features of interest stand out.
- **Normalization**: Standardizing the image scale or intensity to create consistency across multiple images for easier analysis.
### 3. **Segmentation**
- **Thresholding**: Convert the image to a binary or multi-level image to isolate objects or regions of interest (e.g., separate a product from the background).
- **Edge Detection**: Detect the edges of objects or features in the image, which is useful for identifying boundaries and contours.
- **Region of Interest (ROI) Selection**: Select specific areas of the image for further processing, focusing only on relevant portions of the image.
### 4. **Feature Extraction**
- **Geometric Features**: Extract measurements like size, shape, position, orientation, and symmetry from the segmented objects.
- **Texture Analysis**: Analyze the texture patterns for roughness, uniformity, etc., to assess the surface quality.
- **Color Analysis**: Extract color information for color-based inspection, ensuring the correct color is used or verifying its consistency.
- **Pattern Recognition**: Recognize patterns, symbols, or specific features to classify parts or detect defects.
### 5. **Object Detection and Classification**
- **Object Detection**: Identify and label objects within the image to confirm their presence or detect defects.
- **Template Matching**: Match the object or part in the image against a predefined template to check for correct shape, size, and orientation.
- **Classification**: Based on the extracted features, classify the objects as good, bad, or categorize them into specific groups (e.g., defective or non-defective).
### 6. **Decision Making**
- **Comparison Against Tolerances**: The extracted measurements, shapes, and features are compared against predefined tolerances or quality standards.
- **Pass/Fail Decision**: Based on the comparison, a decision is made whether the product meets the required quality standards. If it fails, the system can trigger corrective actions (e.g., rejecting the item or sending it for rework).
- **Real-time Feedback**: Provide real-time feedback to the production system to either pass or reject the part or trigger alarms if defects are detected.
### 7. **Post-processing and Output**
- **Data Logging**: Record the inspection data and images for further analysis or auditing purposes.
- **Output to Control Systems**: The decision is communicated to automated systems such as conveyor belts, robotic arms, or quality control stations to handle the product accordingly.
- **Operator Interface**: The results and images are often displayed on a graphical interface for human operators to monitor the process.
### 8. **Feedback and Learning (Optional)**
- In some advanced systems, **machine learning** or **AI algorithms** are used to adapt and improve decision-making over time by learning from previous images and inspection outcomes.
This image processing pipeline ensures fast, accurate, and repeatable inspection in manufacturing environments, reducing human error and improving overall product quality.